-----------------------------------------------------------------

The following is a news release from Master Bond Inc. You have received it because you are listed as an editor for your publication.

Attached to this email is a low resolution version of the photograph that is included in the press kit for this product.

High resolution version of this image and files with the body text of this release in Word, HTML and text formats are available at http://www.masterbond.com/newsrelease/ep29lphe.

-----------------------------------------------------------------

## FOR IMMEDIATE RELEASE

Two Part, Low Viscosity Epoxy Offers Long Working Life and High Elongation

Master Bond EP29LPHE is a two component epoxy system with a low mixed viscosity of 350-700 cps. This low shrinkage/low exotherm product is particularly well suited for large volume casting applications as well as bonding, coating and sealing. “What sets EP29LPHE apart from other epoxies is that while it cures relatively rigid, it has excellent toughness, provides a low moduls and high elongation, which allows it to withstand shock and impact,” said Rohit Ramnath, senior product engineer. This compound features a Shore D hardness of 50-60 and a tensile elongation of 100-150% at room temperature.

As a two part system, EP29LPHE has a forgiving 100 to 80 mix ratio by weight and has an exceptionally long working life of 12-24 hours at room temperature for a 100 gram batch. It will cure at room temperature or more rapidly at elevated temperatures. This system bonds well to a wide variety of substrates including metals, ceramics, glass, composites, rubbers and plastics, including fiber reinforced plastics and optical fibers.

EP29LPHE has superb optical clarity and light transmission properties. It resists exposure to chemicals including water, acids, bases, oils and fuels. Most notable is that it is a dependable electrical insulator with a volume resistivity of >1015 ohm-cm. Its temperature resistance is from -60°F to +250°F [-51°C to +121°C]. EP29LPHE is available for use in ½ pint, pint, quart, gallon and 5 gallon container kits.

Master Bond Low Exotherm Adhesives

EP29LPHE is a low viscosity epoxy system that features a long working life, reliable electrical insulation and low exotherm suitable for large potting and encapsulation applications. Read more about Master Bond’s low exotherm adhesives at http://www.masterbond.com/properties/low-exothermic-epoxy-systems or contact Tech Support. Phone: +1-201-343-8983 Fax: +1-201-343-2132 Email: technical@masterbond.com.

About Master Bond

Since its founding in 1976, Master Bond has been committed to developing epoxies, silicones, light curing systems and other specialty adhesives that meet specific customer requirements. Master Bond manufactures over 3,000 grades of specially designed formulations that are widely used across a variety of industries including electronic, medical, aerospace and optical.

Note to Editors:

For a full product description, please visit: http://www.masterbond.com/tds/ep29lphe

Check out product videos on our YouTube channel: http://www.youtube.com/user/MasterBondVideo

You can embed any of our videos on your website.

CONTACT

James Brenner, Marketing Manager

Email: jbrenner@masterbond.com

Tel: +1-201-343-8983

Fax: +1-201-343-2132

MASTER BOND INC

154 Hobart Street

Hackensack, NJ 07601-3922

Web: www.masterbond.com